## Slide 1
  —
    Modeling Decarbonization Scenarios of the Building Stock in Germany: an Agent-Based Approach
      Şirin Alibaş, Songmin Yu
      03.06.2024

## Slide 2: Scenario development
Overview of the three scenarios for RokiG
 | Category 1 Energy-efficient building refurbishment as a core component of the energy transition | Category 2 Integration of the individual building into the overall system | Category 3 New construction as a driver of innovation | Category 4 Regulatory framework | Category 5 Society and Economy
Scenario 1 Sustainable transformation in the building sector | Serial renovation is widely adopted from 2030. Low-temperature district heating is widely used. Digitalization of timetables for the whole building. Buildings as prosumers. | DSM technologies adopted by most large electricity consumers. Smart meters are widely adopted. | High efficiency increase in technological progress. Climate-neural operation is obligatory for new buildings and partly implemented in existing buildings. Solar obligation for all new buildings (80% of roof area). | Funding for the promotion of climate-neutral construction and heat-generators are well distributed. Minimum 80% RE in every newly installed heating system. KfW EH 100 requirements. | Enough supply of skilled workers. Supply-chain well managed. Inequality reduced and subsidies granted to right target groups. The idea of communal living gets popular.
Scenario 2 Challenges in transition and varied progress | Serial renovation is widely adopted from 2045. Low-temperature district heating is partly used. Digitalization of timetables for specific components. Buildings prefer HPs. | No flexibility from buildings but only from large central storage facilities. Smart meters are partially adopted by new buildings. | Medium efficiency increase in technological progress. Climate-neural operation is obligatory for new buildings. Solar obligation for all new buildings (60% of roof area). | Funding is not distributed well and lack of long-term orientation. Minimum 65% RE in every newly installed heating system. KfW EH 75 requirements. | Supply of skilled workers is behind target level. Supply-chain partly managed. Inequality has not decreased. The number of old households increases, while the other households stay stable.
Scenario 3 Skills shortage and uncertainties in the building stock development | Serial renovation starts to take shape in 2045. Low-temperature district heating is not used. Digitalization of timetables for not developed. Buildings prefer fossils. | No flexibility. Smart meters are not adopted even by new buildings. | Low efficiency increase in technological progress. Climate-neural operation is not mandatory. Solar obligation not enforced. | Funding is limited and only for specific objectives. No tightening of the current RE requirements. No requirements on building efficiency. | Clear shortage of skilled workers. Supply-chain not well managed. Inequality is clearly greater. Single-person households increases resulting higher demand of living space.
Bagheri, M.; Dönitz, E; Yu, S.; Brugger, H. (2024) Exploration of qualitative scenarios towards climate neutrality of the German building sector, eceee summer study

## Slide 3: Scenario development
Scenario Modeling: modernization of the building envelope
 | Category 1 Energy-efficient building refurbish-ment as a core component of the energy transition | Category 2 | Category 3 New construction as a driver of innovation | Category 4 Regulatory framework | Category 5 Society and Economy
How details are modeled in the building agent ...
  Initialization of buildings: according to the construction period, with the renovation history of each component.
  Simulation of scenarios: buildings are triggered to renovate the components by replacing them with the available options, due to: (1) lifetime reached, or (2) efficiency requirement (mandatory renovation). Labor and material demand is recorded.
  The energy-cost saving of renovation is considered when comparing different options.
How qualitative scenario assumptions are quantified ...
An “availability table” is used to introduce the minimum energy performance standard (MEPS) of building components.
Availability, cost, labor and material demand are distinguished in the scenario tables according to action types of new construction and renovation (conventional or serial). Efficiency and renewable energy requirements also defined for actions.
Conventional and serial renovation are separately considered and quantified.

## Slide 4: Scenario development
Scenario Modeling: modernization of the heating system
 | Category 1 Energy-efficient building refurbish-ment as a core component of the energy transition | Category 2 Integration of the individual building into the overall system | Category 3 | Category 4 Regulatory framework | Category 5 Society and Economy
How details are modeled in the building agent ...
  Supply temperature and contribution of heating technologies are defined for space and water heating, also considering the type of radiator. Heating and cooling demand are calculated with 5R1C model (ISO 13790) in hourly resolution, which also decides the system size. Internal set temperature depends on the buildings‘ efficiency class.
  Each technology can be replaced due to (1) end-of-life reached, or (2) renewable energy requirement (mandatory replacement). Labor demand is recorded.
How qualitative scenario assumptions are quantified ...
Availability table to ban specific technologies in specific years. Infrastructure availability/expansion is considered to decide if district heating and gas network are available during replacement (Geo-resolution: settlement types within NUTS 3 region.)
By calculating heating and cooling demand hourly, the HP profiles can be considered, and the flexibility supported by thermal storage (hot water tanks and building) can be captured.
The efficiency improvement of heating technologies over time is applied as exogenous input.

## Slide 5: Scenario development
Scenario Modeling: impact of behavior change on energy demand
 | Category 1 | Category 2 Integration of the individual building into the overall system | Category 3 | Category 4 | Category 5 Society and Economy
How details are modeled in the building agent ...
  Buildings are initialized with living/working units. Demand profiles of appliance electricity and hot water are assigned to the unit users, as well as their building occupancy profiles. They are aggregated from unit- to building-level.
  The FLEX-Behavior model can be used to develop behavior profiles for households.
  Building occupancy profiles can probabilistically impact the set temperature in each hour, which then impacts the heating and cooling demand calculated by the 5R1C model.
How qualitative scenario assumptions are quantified ...
The efficiency change of electric appliances are considered as an exogenous time-series of efficiency index. It shifts up and down the appliance electricity load profiles.
Teleworking scenarios can be reflected by the occupancy profiles of unit users.
Diffusion of smart energy management system (SEMS) can be partly reflected by the probability that room temperature is set according to the occupancy profile. Also, the model can interact with FLEX-Operation model to capture prosumaging.

## Slide 6: Scenario development
Scenario Modeling: distributional impact and just transition
 | Category 1 | Category 2 | Category 3 | Category 4 | Category 5 Society and Economy
How details are modeled in the building agent ...
  The households (unit users in residential buildings) are assigned with socio-demographic information, e.g., person number, age, working status, income group, role of building owner or tenant, etc.
  The possibility of being triggered to do building renovation and technology replacement, as well as the available options, can be filtered by the socio-demographic information, e.g., due to financial constraint, incentives, etc.
How qualitative scenario assumptions are quantified ...
Subsidy schemes can be introduced and targeting on specific social groups.
The distributional impact of policies can be assessed.
The household sizes can be captured by the “person number” of the “unit users” in the model, then reflected by the demand of new buildings.

## Slide 7: Input from other work packages
AP 4.1: Energy-efficient building refurbishment as a core component of the energy transition
 |  | Feature/handling in model | Related input table
AP 4.1: Energy-efficient building refurbishment as a core component of the energy transition | Influence of serial refurbishment to increase the refurbishment rate (where are the limits) | Serial renovation considered as an option of renovating via: higher component costs, reduced labor demand (craftsman) | Scenario_BuildingComponent_Cost_Material Scenario_BuildingComponent_Input_Labor.xlsx
 | Influence of a lower district heating temperature: where do problems arise in existing buildings | Supply temperature of space heating according to radiator type and building efficiency class | Parameter_Building_SupplyTemperature
 | Influence of renovation roadmaps and their follow-up by the authorities | Mandatory renovation & certain time-window for implementation. | Scenario_Renovation_MaximumHeatingIntensity (time-window of 10 years for implementation.)
 | High influence of energy prices on the choice of the optimal energy system in existing buildings | Operational costs are taken into account via the utility function (the choice is made accordingly.) Exogenous PV penetration rates in existing buildings. | Choice of heating technology via utility function. Decisions are based on a discrete choice model: each separate alternative/option has a “utility” for the user. Utility is calculated via a function considering investment costs, savings in running costs, lifetime of the option, etc.
 | High influence of electricity demand (appliance use, lighting) in non-residential buildings on the choice of the optimal energy system in existing buildings | Relates to higher PV adoption in NRES than RES. Exogenous PV penetration rates in existing buildings. | 
 | Future increase in cooling demand due to changes in outside temp. | Hourly cooling demand calculated acc. to the norm (ISO 13790) | Hourly weather temperature & radiation profiles are used.
 | Rising electricity demand in existing buildings due to heat pumps and electromobility, among other things | Diffusion of HPs due to renewable energy req. and cost advantages. Electromobility not included. | Scenario_HeatingSystem_MinimumRenewablePercentage.xlsx Choice of heating technology via utility function as mentioned above.

## Slide 8: Input from other work packages
AP 4.2: New construction as a driver of innovation
 |  | Feature/handling in model | Related input table
AP 4.2: New construction as a driver of innovation | Influence of a possible legal requirement that new buildings must be climate-neutral in operation | Min. renewable percentage 100% for new buildings | Implemented in the code.
 | Influence of a possible legal requirement that new buildings must have an energy plus (e.g. for feeding into the grid or use for e-mobility) | PV mandatory in new buildings (energy-plus/negative isn’t calculated or guaranteed.) Electromobility not included. | Implemented in the code.
 | Influence of a possible solar obligation (PV) for new buildings | PV mandatory in new buildings. | Implemented in the code.
 | Highlighting individual technologies researched in the building projects and scaling them to a proportion of new buildings or renovated buildings | More input on specific “researched” technologies needed. Currently not modeled. | Discussion needed

## Slide 9: Input from other work packages
AP 4.3: Smart building operation
 |  | Feature/handling in model | Related input table
AP 4.3: Smart building operation | Savings and additional costs through smart building operation throughout Germany (scaling based on the results of the cross-evaluation) | Efficiency gain due to smart operation (new heating tech such as 511: smart operated HP) can be implemented (reasonable/empirical assumptions?) Input on smart device costs? | Discussion needed

## Slide 10: Input from other work packages
AP 4.4: Integration of the individual building into the overall system
 |  | Feature/handling in model | Related input table
AP 4.4: Integration of the individual building into the overall system | Impact of rising gas prices on the speed of electrification in the building sector due to the implementation of heat pumps and electric cars. Thus also increased load on distribution grids due to high simultaneity | Choice of heating technology via utility function considering investment and running costs/savings. Results include the electricity demand. Electromobility not included. | 
 | Decrease in flexibility on the electricity generation side due to possible conversion of gas-fired power plants to coal-fired power plants -> increase in flexibility requirements on the end consumer side (buildings) | The model can interact with FLEX-Operation model to capture prosumaging (external coupling.) | 
 | Influence of digitalization progress in the building sector on demand-side management potential in this sector | Diffusion of SEMS can be partly reflected by the probability that room temperature is set according to the occupancy profile. Also, the model can interact with FLEX-Operation model to capture prosumaging (external coupling.) | 

## Slide 11: Input from other work packages
AP 5: Considerations of regulatory framework conditions
 |  | Feature/handling in model | Related input table
AP 5: Considerations of regulatory framework conditions | Influence of the changed subsidy programs (Efficiency House 55/40 before and after 2022) | Support program considered via reduction on component investment costs | Scenario_Subsidy_HeatingModernization.xlsx & Scenario_Subsidy_BuildingRenovation.xlsx
 | Influence of a simplified tenant electricity principle | Not included yet. More input needed on how the “Mieterstromprinzip” works? | Note: If operational cost is important, we can have the effect of lower electricity cost via PV. However, this won’t be considered in investment decision as the PV penetration rate will be exogenous.
 | Influence of refurbishment constraints / stricter minimum requirements for building refurbishment. See also above under new construction requirements | Thermal performance requirements for materials in renovation are getting stricter in time. Stricter thermal performance requirements for materials in new construction as well. | Scenario_BuildingComponent_Availability
 | Influence of technology bans, e.g. gas (additional costs, possible savings) | Available heating technologies at the year of installation/replacement are defined by the input table | Scenario_HeatingTechnology_Availability.xlsx